## Slide 1
Sun Yat-sen University | 中山大学
Sino-French Institute of Nuclear Engineering and Technology
Study of Radioactive Source Monitoring Based on ElasticNet Regression Method
基于弹性网络回归算法的放射源监测研究
Candidate: Wang Kaiqi (王开齐) | Student ID: 22355080
Supervisors: Prof. Shi Wei (CityU HK) & Prof. Wang Kai (SYSU)
Major: Nuclear Engineering and Nuclear Technology
Bachelor's Thesis Defense | April 2026

## Slide 2
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Outline
2 / 20
01
Research Background & Problem Statement
02
Literature Review: LASSO, Fused LASSO, and Alternatives
03
Theoretical Basis: Ill-posed Systems & ElasticNet Formulation
04
Algorithm Implementation & Optimization Strategies
05
PHITS Monte Carlo Simulation & Contribution Matrix
06
Numerical Experiments: Benchmark Validation
07
PHITS Physical Validation Results
08
Bayesian Optimization Experiments
09
Conclusions & Future Work

## Slide 3
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Research Background
Nuclear facility decommissioning & emergency response
3 / 20
▸ Nuclear decommissioning is growing worldwide (Fukushima Daiichi, etc.)
▸ IAEA: Accurate source distribution is prerequisite for optimized decommissioning
▸ Three-dimensional complexity of radioactive sources in confined spaces:
(1) Composite source types: localized hot-spots + continuous activation zones + dispersed media
(2) Nuclide diversity: ¹³⁴Cs, ¹³⁷Cs, ⁶⁰Co, ¹³¹I — different energy spectra & biological effects
(3) Measurement constraints: limited detectors, limited time, dose exposure limits
▸ The inverse reconstruction problem is both underdetermined (m < n) and ill-posed
▸ A single method must: locate sparse hotspots, reconstruct continuous regions,
distinguish nuclides, and be computationally efficient for field deployment

## Slide 4
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Literature Review
Existing methods and their limitations
4 / 20
Method
Sparse Loc.
Continuous Region
Multi- nuclide
Computation
Core Limitation
ML-EM / MPMI (Sugaya et al.)
Fair
Good
Poor
Slow
O(n³) cost; noise sensitive; no sparsity mechanism
IRT-DEGL (Chen et al.)
Fair
Fair
Fair
Very slow
Global optimization: massive sampling required
LASSO (Shi et al., JAEA)
Excellent
Poor
Good
Fast
Over-compresses continuous regions to discrete points
Fused LASSO (Yamada et al.)
Fair
Good
Good
Medium
Needs predefined neighborhood graph; ADMM complexity
ElasticNet (This work)
Excellent
Excellent
Good
Fast
First application in nuclear source monitoring
Table 1: Comprehensive comparison of radioactive source reconstruction methods

## Slide 5
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
ElasticNet Regression: Theory
Combining L1 and L2 regularization (Zou & Hastie, 2005)
5 / 20
Objective Function: min ||y - Xw||²₂ + α · [ ρ · ||w||₁ + (1-ρ)/2 · ||w||²₂ ] α = overall regularization strength ρ (l1_ratio) = L1/L2 mixing ratio
▸ L1 Penalty (ρ · ||w||₁):
• Promotes sparsity — counts non-zero elements
• Drives irrelevant coefficients to exact zero
• Enables hot-spot localization
▸ L2 Penalty ((1-ρ)/2 · ||w||²₂):
• Groups correlated variables together
• Suppresses oscillation and overfitting
• Preserves continuous region morphology
▸ Synergy Effect:
• Near sparse hotspots: L1 dominates → precise localization
• Inside continuous regions: L2 dominates → smooth reconstruction
• Transition zones: both cooperate → natural morphological transition
▸ Key Properties:
• Strictly convex (when λ₂ > 0) → unique global minimum
• No ADMM convergence issues (unlike Fused LASSO)
• Solved by Coordinate Descent algorithm
• ρ → 1: degrades to LASSO; ρ → 0: degrades to Ridge

## Slide 6
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Algorithm Implementation Pipeline
Preprocessing → Optimization → Post-processing
6 / 20
Stage 1: Preprocessing
• Column normalization of A
(scale each column to unit L₂ norm)
• Non-negative SVD matrix construction
• Condition number assessment
• Adaptive α search range selection:
cond=100: α ∈ [10⁻⁶, 10⁰]
cond=500: α ∈ [10⁻⁵, 10¹]
cond=1000: α ∈ [10⁻⁴, 10²]
Stage 2: Optimization
• ElasticNet with positive=True
(hard non-negativity constraint)
• GridSearchCV parameter search:
α: 50 values (log scale)
l1_ratio: 80 values (linear)
5-fold cross-validation
• Scoring: neg_MSE with intercept
penalty for |β₀/ȳ| > 10%
• Coordinate Descent solver
(max_iter=20000, tol=10⁻⁸)
Stage 3: Post-processing
• Denormalize: w_est = w_norm ⊘ col_norms
• Non-negative truncation
• Intercept analysis: |β₀/ȳ| ratio
• Evaluation metrics:
- MSE, R², Pearson correlation
- Sparsity match ratio
- Per-cell relative error

## Slide 7
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
PHITS Monte Carlo Simulation
Contribution matrix construction with real physics
7 / 20
▸ PHITS (JAEA): Monte Carlo particle transport code
▸ Simulates photon transport in 3D geometry
▸ Cs-137 point sources (0.662 MeV γ-ray)
▸ Simulation: 10⁸ particles × 100 batches
▸ Geometry Configuration:
• Spherical space (R=10m, centered on reactor)
• 10 scattered point sources → mapped to 12 grid cells
• 4 columns × 3 rows floor grid
• 8 spherical detectors (R=25mm) at z=20mm
• Medium: air (N, O, Ar at standard density)
▸ Contribution Matrix A (8×12):
• Only 11/96 elements non-zero (11.5%)
• Matrix rank = 6/8 → significant information loss
• Multiple blind-spot cells
Source-Detector Configuration
• Sources: 10 Cs-137 point sources, 1 Ci each
• Grid: 12 cells (4×3), cell size ~150mm × 200mm
• Detectors: 8 spheres, R=25mm, distributed around perimeter
• Active cells: 7 of 12 (Cell 0,1,5,6,7,8,9,10)
• Zero-response cells: Cell 3,4,11 (detector blind spots)
• Contribution matrix rank: 6/8
• Fragment spread: log-normal distance distribution
• Activity decay: exponential with distance

## Slide 8
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
PHITS Validation Results
8×12 underdetermined system with real physics
8 / 20
▸ Best parameters: α = 1.0×10⁻⁶, l1_ratio = 0.99
▸ Overall R² = 0.463
▸ All 7 non-zero cells successfully detected (no missed detections)
▸ 5 of 7 cells: relative error < 2%
Cell
True Activity (GBq)
ElasticNet Estimate (GBq)
Relative Error
Cell 1
1.265×10⁵
1.265×10⁵
0.0%
Cell 5
5.266×10⁴
3.93×10²
99.3%
Cell 6
1.192×10⁵
2.31×10³
98.1%
Cell 7
5.894×10⁴
5.894×10⁴
0.0%
Cell 8
5.724×10⁴
5.724×10⁴
0.0%
Cell 9
4.870×10⁴
4.870×10⁴
0.0%
Cell 10
1.352×10⁵
1.373×10⁵
1.2%
⚠ Cell 5 & Cell 6 errors stem from detector geometry (weak response, not algorithm defect)

## Slide 9
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Intercept Fitting & Noise Tolerance
Trade-off between generalization and reconstruction quality
9 / 20
▸ fit_intercept=True allows model to learn constant offset (baseline noise level)
▸ Beneficial cases (|β₀/ȳ| < 10%):
✓ Improved generalization to noisy measurement data
✓ Captures background radiation baseline
✓ Prediction MSE extremely low
▸ Problematic cases (|β₀/ȳ| >> 10%):
✗ Intercept dominates → reconstruction degrades significantly
✗ Model 'cheats' by fitting noise offset rather than true source structure
✗ Prediction MSE still very low, but actual reconstruction MSE is poor
▸ Custom scoring function to penalize large intercept ratios:
• |β₀/ȳ| < 1%: penalty factor = 0.9
• 1% ≤ |β₀/ȳ| < 10%: penalty factor = 1.0 (optimal range)
• 10% ≤ |β₀/ȳ| < 15%: penalty factor = 0.6
• |β₀/ȳ| ≥ 15%: penalty factor = 0.3
▸ Key finding: ElasticNet has an upper limit of noise tolerance
Beyond this limit, neither fit_intercept=True nor False gives good results

## Slide 10
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Optimization Strategies for Different Condition Numbers
Chapter 5: Systematic exploration
10 / 20
▸ Experimental design: condition numbers 50–500, 10 random trials each
▸ Discovery: difficulty 'inflection points' at cond ≈ 150 and cond ≈ 300
▸ Not simply 'more ill-conditioned = harder' — special spectral structure at these points
Adaptive CV Folds
• Dynamic CV fold selection based on condition number • Effective for low cond • Limited for high cond (≥300)
Segmented α Search
• Divide α range into segments • Dense search in difficult zones • Medium cond improvement • Still unstable at cond 350+
Fusion Strategy
• Partition by condition number • Apply best strategy per zone • Weighted result fusion • Cannot break upper bound at high cond
Bayesian Optimization
• GP surrogate model • gp_hedge acquisition function • 40 evaluations (vs 150-450) • 70-90% computation savings • Complementary to grid search

## Slide 11
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Bayesian Optimization: Method & Results
Gaussian Process-based hyperparameter search
11 / 20
▸ GP surrogate model for f(α, ρ)
▸ gp_hedge acquisition function:
Dynamically switches between:
- Expected Improvement (EI)
- Lower Confidence Bound (LCB)
- Probability of Improvement (PI)
▸ 40 evaluations vs. 150-450 for grid search
▸ Converges within 10-15 iterations to
within 5-10% of final optimum
▸ Results:
• Low cond (≤150): matches grid search
• High cond (≥300): slightly worse than
exhaustive grid search
• Core advantage: 5-10× faster
▸ PHITS Validation with Bayesian:
• Same 8×12 contribution matrix
• Strong-signal cells (1,7,8,9): accurate
• Weak-signal cells (5,6): 'selective zeroing'
• Consistent with Ch.5 findings
▸ Key Conclusion:
Bayesian optimization and grid search
are complementary, not substitutive:
• Grid search: higher accuracy ceiling
(exhaustive, finds cross-order optimum)
• Bayesian: faster convergence
(ideal for rapid iteration / auto-tuning)
▸ Best l1_ratio consistently ≈ 0.99
→ confirms strong sparsity prior in
this inverse problem

## Slide 12
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Condition Number Impact & Difficulty Inflection Points
12 / 20
▸ Column normalization is the numerical foundation for all subsequent optimizations
• Balances contribution weights across columns in cost function
• Does NOT directly reduce condition number, but stabilizes parameter search path
▸ Adaptive α search range (key optimization):
• Cond = 100: α ∈ [10⁻⁷, 10⁰] → MSE < 10⁻³ achieved
• Optimal l1_ratio ≈ 0.99 across all conditions → strong sparsity is the true prior
▸ Difficulty inflection points at cond ≈ 150 and 300:
• Special spectral noise amplification structure
• Not simply 'higher cond = harder' — critical matrix structure matters
• All strategies show marginal diminishing returns at these points
▸ Robustness challenge remains:
• Under same conditions, different random seeds yield R² variance > 0.5
• Algorithm excels for certain source distributions but fails for others
• This is the core obstacle for practical deployment

## Slide 13
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
ElasticNet Applications in Related Fields
Cross-domain evidence supporting L1+L2 synergy
13 / 20
Nuclear Medicine (Kasai & Otsuka, 2025)
• Dynamic ElasticNet in MLEM
framework for SPECT imaging
• Outperforms pure L1, L2, and
fixed-weight ElasticNet
• Better noise suppression +
fine structure preservation
XLCT Imaging (Zhao et al., 2021)
• X-ray luminescence computed
tomography reconstruction
• L1+L2 resists over-sparsity
and over-smoothing
• Superior localization, dual-source
resolution, and robustness
Fluorescence Molecular Tomography (Zhang et al.)
• APSEN method for FMT
• 30%+ reduction in localization
error vs comparison methods
• Validated in phantom and
in-vivo experiments
→ These cross-domain studies confirm: ElasticNet's L1+L2 design has inherent superiority in handling the 'sparse vs. continuous' contradiction — motivating its application to nuclear source monitoring

## Slide 14
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Conclusions
14 / 20
1
ElasticNet fills the application gap in nuclear source monitoring, effectively handling the 'sparse + continuous' composite source reconstruction scenario.
2
Optimization strategies (column normalization, adaptive α, non-negative constraint, intercept penalty) significantly improve accuracy: cond 100-300 all achieve good fit.
3
PHITS validation: all 7 non-zero cells detected, 5 cells with < 2% error. Cell 5/6 errors originate from detector layout, not algorithm deficiency.
4
Difficulty inflection points at cond ≈ 150, 300 identified. All strategies show diminishing returns at high condition numbers. Fusion cannot break the performance ceiling.
5
Bayesian optimization is complementary to grid search: 70-90% computation savings, suitable for rapid iteration; grid search provides higher accuracy ceiling.

## Slide 15
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Future Work & Outlook
15 / 20
▸ Mobile Detection Platforms (UGV / UAV):
• Carry detectors for large-scale autonomous patrol in plant buildings
• Acquire radiation signals at multiple spatial positions → richer contribution matrix
• Greatly reduce matrix condition number → improve ElasticNet stability
▸ Algorithm Improvements:
• Adaptive ElasticNet for automatic variable selection
• Bayesian ElasticNet with uncertainty quantification
• Dynamic regularization combined with deep learning feature extraction
• Model cascade: DL feature extraction → ElasticNet reconstruction
▸ Extended Applications:
• Multi-energy source discrimination (different nuclides)
• 3D volumetric source reconstruction
• Mobile detector path planning optimization
• Real-time online source reconstruction system
▸ From simulation to field deployment — pushing toward engineering applications

## Slide 16
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Selected References
16 / 20
[1] Tibshirani R. Regression shrinkage and selection via the lasso. JRSS-B, 1996.
[2] Hoerl & Kennard. Ridge regression: Biased estimation for nonorthogonal problems. Technometrics, 1970.
[3] Sugaya et al. Inverse estimation methods of unknown radioactive source for fuel debris search. ANE, 2019.
[4] Shi W et al. LASSO reconstruction with spectral information. ANE, 2023.
[5] Shi W et al. Inverse estimation using LASSO: Theory and demonstration. PNE, 2023.
[6] Machida et al. Observation point selection using Bayesian LASSO. EPJ Web Conf., 2024.
[7] Yamada et al. Effectiveness of Fused LASSO for radioactive distribution prediction. WM2024.
[8] Zou & Hastie. Regularization and variable selection via the elastic net. JRSS-B, 2005.
[9] Kasai & Otsuka. Iterative reconstruction with dynamic elastic net. J. Imaging, 2025.
[10] Zhao et al. Robust elastic net for XLCT. Phys. Med. Biol., 2021.
[11] Friedman et al. Regularization paths via coordinate descent. JSS, 2010.
[13] Sato et al. PHITS version 3.02. JNST, 2018.
[14] Shahriari et al. Taking the human out of the loop: Bayesian optimization review. Proc. IEEE, 2016.

## Slide 17
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Source-Detector Geometry Detail
Fragment simulation → floor grid mapping
17 / 20
▸ Fragment Distribution Simulation:
• Distance: log-normal distribution
• Angle: uniform random [0, 2π]
• Activity: exponential decay with distance
• A = A₀ · exp(-β · {distance factors})
▸ Floor Grid Mapping (4×3 = 12 cells):
• X: [-2400, -1800] mm → 4 columns
• Y: [100, 700] mm → 3 rows
• Multiple sources in same cell:
activities are summed (linear叠加)
▸ 7 active cells, 5 empty cells
Source Parameters (10 point sources)
S0(-1824,337)→Cell(1,3) w=0.863
S1(-1993,510)→Cell(2,2) w=1.000
S2(-2051,475)→Cell(2,2) w=0.920
S3(-2072,390)→Cell(2,1) w=0.825
S4(-2048,515)→Cell(2,2) w=0.980
S5(-2170,123)→Cell(1,0) w=0.884
S6(-2172,330)→Cell(1,1) w=0.771
S7(-2243,175)→Cell(1,0) w=0.968
S8(-2198,624)→Cell(1,2) w=0.713
S9(-2255,632)→Cell(0,2) w=0.838

## Slide 18
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Error Source Analysis
Why some cells fail — it's the physics, not the algorithm
18 / 20
▸ Cell 6 (true: 1.19×10⁵ GBq, estimated: 2.31×10³ GBq, error: 98.1%):
• Only Detector 1 has response — and extremely weak (10⁻⁹ MeV/cm³/source level)
• Signal completely overwhelmed by stronger responses from other cells
▸ Cell 5 (true: 5.27×10⁴ GBq, estimated: 3.93×10² GBq, error: 99.3%):
• Only Detector 5 has weak response (10⁻¹⁰ level)
• Same issue: single-detector, extremely weak signal
▸ Matrix rank analysis: A has numerical rank = 6/8
• Only 6 of 12 cells are algebraically distinguishable
• Remaining cells' information is completely lost in detector response
• This is physical indistinguishability from detector geometry, NOT algorithm failure
▸ Implication: improved detector layout (more positions, better coverage) would
directly resolve these errors — ElasticNet itself is not the bottleneck

## Slide 19
Sun Yat-sen University | Sino-French Institute of Nuclear Engineering
Research Objectives — Achievement Summary
19 / 20
Objective 1
Establish mathematical model for composite source reconstruction
✅ Achieved: L1 for sparse + L2 for continuous, synergy mechanism clarified
Objective 2
Systematic algorithm validation under realistic constraints
✅ Achieved: PHITS simulation, condition number 50-500, 10 trials × 10 conditions
Objective 3
Feasibility assessment for field deployment
✅ Achieved: identified noise tolerance ceiling, detector layout as key factor, UGV/UAV pathway

## Slide 20
Thank You!
谢谢各位老师！
Questions & Discussion
Wang Kaiqi (王开齐) | 22355080 Sino-French Institute of Nuclear Engineering and Technology Sun Yat-sen University (中山大学) Supervisors: Prof. Shi Wei (石巍) — City University of Hong Kong Prof. Wang Kai (王凯) — Sun Yat-sen University