## Slide 1
SYSU
Sun Yat-sen University
Study of Radioactive Source Monitoring Based on ElasticNet Regression Method
Bachelor's Thesis Defense Report
Wang Kaiqi
Sino-French Institute of Nuclear Engineering and Technology, Sun Yat-sen University
Supervisors: Prof. Shi Wei (CityU HK) & Prof. Wang Kai (SYSU)
April 2026

## Slide 2
SYSU
Outline
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 1 / 25
1 Background & Motivation
2 Literature Review
3 Theoretical Basis
4 Algorithm & Optimization
5 PHITS Simulation
6 Results & Analysis
7 Conclusions & Future Work
References
Q & A

## Slide 3
SYSU
Research Background
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 2 / 25
Nuclear Facility Decommissioning
• Global decommissioning projects increasing (Fukushima Daiichi, etc.)
• IAEA: Accurate source distribution is prerequisite for optimized decommissioning
Three-Dimensional Complexity
• Composite sources: localized hot-spots + continuous activation + dispersed media
• Nuclide diversity: ¹³⁴Cs, ¹³⁷Cs, ⁶⁰Co, ¹³¹I
• Constraints: limited detectors, time, dose limits
Core Challenge
• The inverse reconstruction problem is both underdetermined (m ≪ n) and ill-posed
• A single method must handle sparse hotspots, continuous regions, and multi-nuclide discrimination

## Slide 4
SYSU
Problem Statement
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 3 / 25
Definition 4.1 Mathematical Formulation
d = A · s + ε where d: measurements, A: contribution matrix, s: source vector, ε: noise
Key Challenges
• Underdetermined: fewer detectors than unknowns (m ≪ n)
• Ill-posed: noisy data leads to unstable solutions
• Mixed: sparse hot spots + continuous activation regions

## Slide 5
SYSU
Existing Methods and Limitations
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 4 / 25
Method | Sparse | Continuous | Multi-n. | Speed | Core Limitation
ML-EM/MPMI | Fair | Good | Poor | Slow | O(n³); noise sensitive
IRT-DEGL | Fair | Fair | Fair | V.Slow | Global optimization cost
LASSO | Exc. | Poor | Good | Fast | Over-compresses continuous
Fused LASSO | Fair | Good | Good | Med. | Needs neighborhood graph
ElasticNet | Exc. | Exc. | Good | Fast | Not yet applied to nuclear
Table: Comparison of radioactive source reconstruction methods

## Slide 6
SYSU
Why ElasticNet?
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 5 / 25
Advantages over LASSO and Fused LASSO
• LASSO: over-compresses continuous regions to discrete points
• Fused LASSO: needs predefined neighborhood graph + ADMM issues
• ElasticNet: L1+L2 synergy without extra spatial constraints
Cross-Domain Evidence
• Nuclear medicine (SPECT): outperforms pure L1, L2, fixed-weight EN
• XLCT imaging: superior localization + dual-source resolution
• Fluorescence molecular tomography: 30%+ error reduction
Theorem 2.1 Research Gap
ElasticNet has NOT been applied to nuclear radioactive source monitoring — this thesis fills that gap.

## Slide 7
SYSU
ElasticNet Regression Formulation
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 6 / 25
Definition 3.1 Objective Function (Zou & Hastie, 2005)
min_w ||y - Xw||²₂ + α [ ρ||w||₁ + (1-ρ)/2 · ||w||²₂ ]
L1 vs. L2 Penalty Roles
• L1: promotes sparsity → hot-spot localization
• L2: groups correlated variables, suppresses oscillation
• ρ → 1: LASSO; ρ → 0: Ridge
Key Properties
• Strictly convex when λ₂ > 0 → unique global minimum
• Solved by Coordinate Descent; no ADMM convergence issues

## Slide 8
SYSU
Physical Interpretation
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 7 / 25
L1: Sparse Hot-Spot Localization
• Count-type penalty on 'how many grid cells contain sources'
• Drives irrelevant coefficients to exact zero
L2: Continuous Region Smoothing
• Suppresses individual amplitude, promotes similar neighboring values
• Preserves continuous region morphology (not discrete spots like LASSO)
Theorem 3.1 Synergy Effect
Near hotspots: L1 dominates → precise localization. Inside continuous regions: L2 dominates → smooth morphology. Transition zones: both cooperate.

## Slide 9
SYSU
Algorithm Pipeline
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 8 / 25
Stage 1: Preprocessing
• Column normalization: scale each column of A to unit L₂ norm
• Non-negative SVD matrix construction
• Condition number assessment for adaptive α range
Stage 2: ElasticNet Optimization
• ElasticNet(positive=True) — hard non-negativity constraint
• GridSearchCV: α (50 values), ρ (80 values), 5-fold CV
• Custom intercept penalty for |β₀/ȳ| > 10%
Stage 3: Post-processing
• Denormalize: w_est = w_norm ⊘ col_norms
• Non-negative truncation, intercept analysis, evaluation metrics

## Slide 10
SYSU
Key Optimization: Column Normalization
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 9 / 25
Figure: Column normalization: cond=100, 5 runs all achieve MSE=10⁻⁴ to 10⁻⁹

## Slide 11
SYSU
Non-negative SVD + Non-negative ElasticNet
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 10 / 25
Figure: Non-negative SVD + non-negative EN: Exp1/Exp3 reach MSE=10⁻⁹

## Slide 12
SYSU
Intercept Fitting Analysis
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 11 / 25
Good case: small intercept
Bad case: large intercept

## Slide 13
SYSU
PHITS Simulation Configuration
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 12 / 25
PHITS (JAEA): Monte Carlo Particle Transport
• 10⁸ particles × 100 batches; Cs-137, 0.662 MeV γ-ray
Parameter | Value
Simulation space | Spherical (R=10m, reactor-centered)
Radioactive sources | 10 Cs-137 point sources, 1 Ci each
Detectors | 8 spherical detectors (R=25mm)
Grid division | 4 × 3 = 12 cells
Contribution matrix | 8 × 12 (only 11/96 non-zero)
Matrix rank | 6/8

## Slide 14
SYSU
Source-Detector Geometry
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 13 / 25
• 10 Cs-137 point sources (1 Ci)
• 4 × 3 = 12 grid cells
• 8 spherical detectors (R=25mm)
• 7 active cells, 5 empty
• Matrix: 8 × 12, rank=6/8

## Slide 15
SYSU
PHITS Validation Results
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 14 / 25
Best: α = 10⁻⁶, l1_ratio = 0.99, R² = 0.463 | 7 non-zero cells detected, 5 with <2% error
Cell | True (GBq) | Estimate (GBq) | Error
Cell 1 | 1.265×10⁵ | 1.265×10⁵ | 0.0%
Cell 5 | 5.266×10⁴ | 3.93×10² | 99.3%
Cell 6 | 1.192×10⁵ | 2.31×10³ | 98.1%
Cell 7 | 5.894×10⁴ | 5.894×10⁴ | 0.0%
Cell 8 | 5.724×10⁴ | 5.724×10⁴ | 0.0%
Cell 9 | 4.870×10⁴ | 4.870×10⁴ | 0.0%
Cell 10 | 1.352×10⁵ | 1.373×10⁵ | 1.2%

## Slide 16
SYSU
Reconstruction Visualization
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 15 / 25
True vs. estimated distribution
Contribution matrix heatmap

## Slide 17
SYSU
Error Source Analysis
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 16 / 25
Cell 5 & 6 Failure — Physical, Not Algorithmic
• Cell 6: only Detector 1 responds, weak signal (10⁻⁹ level)
• Cell 5: only Detector 5 responds, weak signal (10⁻¹⁰ level)
Theorem 6.1 Matrix Rank Analysis
Rank of A = 6/8. Only 6 of 12 cells algebraically distinguishable. Physical indistinguishability from detector geometry, NOT algorithm failure.
Implication
• Improved detector layout would resolve these errors. ElasticNet is NOT the bottleneck.

## Slide 18
SYSU
Condition Number Impact
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 17 / 25
Figure: Comparison of adaptive CV, segmented search, and fusion strategies

## Slide 19
SYSU
Bayesian Optimization Results
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 18 / 25
Bayesian opt.: sparse source
Bayesian + PHITS validation

## Slide 20
SYSU
Grid Search vs. Bayesian Optimization
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 19 / 25
Difficulty Inflection Points at Cond ≈ 150 and 300
• Not 'more ill-conditioned = harder' — critical spectral structure matters
• Optimal l1_ratio ≈ 0.99 universally — confirms strong sparsity prior
 | Grid Search | Bayesian Opt.
Evaluations | 150–450 | 40
Speed | Baseline | 5–10× faster
Accuracy (low cond) | Reference | Comparable
Accuracy (high cond) | Higher ceiling | Slightly worse
Complementary, not substitutive

## Slide 21
SYSU
Conclusions
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 20 / 25
1. ElasticNet fills the application gap
• Effectively handles 'sparse + continuous' composite source reconstruction.
2. Optimization strategies improve accuracy
• Column normalization + adaptive α + non-negative constraint + intercept penalty.
3. PHITS validation confirms practical value
• All 7 non-zero cells detected; 5 cells with <2% error.
4. Bayesian optimization: complementary to grid search
• 70–90% computation savings; grid search has higher accuracy ceiling.

## Slide 22
SYSU
Future Work
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 21 / 25
Mobile Detection Platforms (UGV / UAV)
• Autonomous patrol → richer contribution matrix → improved stability
Algorithm Improvements
• Adaptive ElasticNet for automatic variable selection
• Bayesian ElasticNet with uncertainty quantification
• Deep learning + ElasticNet model cascade
Extended Applications
• Multi-energy source discrimination & 3D volumetric reconstruction
• Real-time online reconstruction system

## Slide 23
SYSU
References
Wang Kaiqi Sino-French Institute of Nuclear Engineering and Technology, SYSU
Study of Radioactive Source Monitoring Based on ElasticNet 22 / 25
[1] Tibshirani R. Regression shrinkage and selection via the lasso. JRSS-B, 1996.
[2] Hoerl & Kennard. Ridge regression. Technometrics, 1970.
[3] Sugaya et al. Inverse estimation for fuel debris search. ANE, 2019.
[4] Shi W et al. LASSO with spectral information. ANE, 2023.
[5] Shi W et al. LASSO: Theory and demonstration. PNE, 2023.
[6] Yamada et al. Fused LASSO for radioactive materials. WM2024, 2024.
[7] Zou & Hastie. Regularization via the elastic net. JRSS-B, 2005.
[8] Kasai & Otsuka. Dynamic elastic net for nuclear medicine. J. Imaging, 2025.
[9] Zhao et al. Robust elastic net for XLCT. Phys. Med. Biol., 2021.
[10] Sato et al. PHITS version 3.02. JNST, 2018.

## Slide 24
SYSU
Questions & Discussion
Thank you for your attention!
Wang Kaiqi | 22355080
Supervisors: Prof. Shi Wei (CityU HK) & Prof. Wang Kai (SYSU)